RDK-B
meta-cmf-arm
Virtualisation guide with virt-manager (GUI)
Author: Mathew McBride <matt@traverse.com.au>

---
System Pre-requisites
Qemu Arm64 installed (qemu-system-aarch64)
Virt-manager installed and functional
A bridge interface for LAN (and optionally, WAN) side interfaces
These instructions have been tested on Ubuntu 24.10
Instructions for ‘headless’ (no GUI manager) setup can be found in the meta-cmf-arm documentation

---
RDK-B build prerequisites
- You will need the “.wic.qcow2” generated by meta-arm-cmf’s rdk-generic-broadband-image
- If you only have the ‘.wic’ file, you can convert to qcow2 with qemu-img:
  qemu-img convert -O qcow2 rdk.wic rdk.qcow2
- To allow upgrades, resize the disk before using it:
  qemu-img resize rdk.qcow2 10G

---
Virtual Networking (1)
It is best to create an “isolated” network to simulate the “LAN” side of the RDK-B router

---
Virtual Networking (2)
- Use the following settings:
  - Mode: Isolated
  - Uncheck ‘Enable IPv4’
  - Uncheck ‘Enable IPv6’

---
Start
At the home screen of Virtual Machine Manager, click the Create a new virtual machine icon in the toolbar

---
Create a new ARM64 VM
- Select Import Existing disk Image
- Expand Architecture Options and select Architecture: aarch64
  - If this option is missing, you need to install qemu-system-aarch64

---
Select RDK-B qcow2 image (1)
In the ‘Locate or create storage volume’ window, click ‘Browse Local’

---
Select RDK-B qcow2 image (2)
- Select the .wic.qcow2 from the RDK-B build on your local filesystem
- Click “Open”
- On first usage, you may get a message asking to modify the security configuration to allow access to the image. Accept this change.

---
Select OS type
In the “Choose the operating” system box at the bottom, search and choose “Generic Linux 2022”

---
Set RAM and CPU allocation
2GB RAM and 2 vCPUs are sufficient

---
Name and customization
- Give the VM a name (like rdkb-arm)
- Ensure Customize configuration before install is checked

---
Choose Non secure boot firmware
IMPORTANT!
- In the firmware dropdown, select the non-secure boot firmware (AAVMF_CODE.no-secboot.fd)

---
Change LAN network
Change the first NIC to be on your isolated LAN network

---
Add a WAN NIC
- Click “Add Hardware” and add a second network controller
- This will be the WAN interface
- NAT is OK for now

---
Finish VM configuration
Click Begin Installation at the top left to finish installation

---
Boot RDK-B
RDK-B will boot inside the virtual machine